## Slide 1
Level 5 West Wing Lab Induction
https://www.ndcn.ox.ac.uk/about/professional-services/health-and-safety/laboratory-safety

## Slide 2
Follow up email will contain: “COSHH_Health_Surveillance_Registration_Form_HS1-1.docx”
  Complete and return the form to the Lab Manager if you work with any of the following:
    Human blood (Hepatitis B vaccination)
    Animal allergens (Lung test and mandatory health questionnaire)
    Reagents linked to occupational disease (glutaraldehyde, solder flux, latex )
    Pathogens (such as Listeria)
Occupational Health

## Slide 3: NDCN Laboratory Rules – Do’s
All Labs are CL2
Request locker to store personal items – email facilities@ndcn.ox.ac.uk
Personal Protective Equipment must be worn:
                Labcoat
                Gloves
                Safety spectacles - for Prescription safety glasses > contact facilities@ndcn.ox.ac.uk
Hands must be washed upon exit from the laboratory.
There is a ‘one glove’ policy for moving between lab areas, therefore, a glove must be removed before using doors.
Clean up spill immediately if this happens
Respect shared equipment (clean up!)
Report any fault to Facilities
Notify Facilities if help is needed

## Slide 4
Strictly no eating, drinking, chewing or cosmetic application within the laboratory or corridor
No clean gloves on door handles
No paper towel on door handles
No open toe shoes.
No re-sheathing of blades or needles
Do not overfill waste bins
Headphones only one ear/low volume only so alarms can be heard
>> Escalation procedure in place for recurrent non compliance
NDCN Laboratory Rules – Don’ts

## Slide 5: Risk Assessment
Assess before you order
  Storage
  Handling
  Disposal
Who is at risk
What is the risk of exposure
What are the control measures
  Fume hood
  Safety cabinet
Record finding
Get DSO review risk assessment
Sign of by supervisor
Review regularly
All new starter must be taken through relevant RA

## Slide 6: Cold room
No cardboard
No paper
Keep item in plastic container
Must be labelled with group name
Keep area clean and clutter free
Clean up any spill
Do not accumulate waste

## Slide 7: Chemical Safety
Flammable liquid must be kept in closed flammable cupboard – 90minute fire retardant provided in laboratory
Limit of 50L per room for highly flammable liquids
Gloves must be suitable for chemical handled – check COSHH risk assessment
Incompatible material:

## Slide 8: Fume cupboard / Weighing station
Local Exhaust Ventilation
Must be kept clear and uncluttered
Min speed 0.4m/s – if not - not safe to use!
If issue – contact Facilities
Local filter – for powdered substance only
Keep uncluttered
Check airflow is on
0.4m/s also
If in alarm – contact Facilities

## Slide 9: Safety cabinet
For biological material
Keep uncluttered – sterile
Check airflow is on
Must not use with solvent
If in alarm – contact Facilities
Clean after use – turn motor off to clean below surface!

## Slide 10
  LN2 is an asphyxiant by displacing Oxygen
    Evacuate the area as soon as the alarm sounds
    NEVER enter the area if the alarms are sounding
  Cold burns and frost bite – must use provided PPE
    Face shield , cryogloves, labcoat for cryotank
    Face shield, cryogloves, labcoat + Apron – dispensing LN2
  Space in the towers is allocated by Facilities – cells placed erroneously could be lost!
Dispensing of LN2: contact facilities for hands-on training
Cryogenics – liquid nitrogen

## Slide 11
  Dry ice – pelleted CO2 – hazardous gas
    Allow dissipate in ventilated area
    Return excess to Card-Ice in corridor
    Never place dry ice in cold room
  Cold burns and frost bite – must use provided PPE
    cryogloves, labcoat and safety glasses
    Never handle with bare fingers
If large volume needed for shipment – contact Facilities team
Emergency procedures (LN2 and dry ice):
  Explosions due to trapped expanding gas
    Never put LN2/dry ice in a sealed container
  Effects on materials: brittle
    Use material design for very low temperatures
  Emergency procedure: run under tepid water for 20min – seek medical help
Cryogenics – dry ice

## Slide 12: Know your emergency procedures!
Biological material
Chemical material
  COSHH
Mechanical hazard
Engineer on site
Need safety overview – with Facilities
Need contact on site (in case of fire alarm in example)
Equipment/area to be decontaminated – segregated from active work

## Slide 13
  Be mindful of container: in ex petri dish is likely spill
  Use rack or box to facilitate transport in lab space
  When transporting biological or chemical substances out of CL2 lab suitable secondary containment MUST be used.
  Cardboard/polystyrene boxes are not suitable as they will not contain liquids!
  Public transport is not suitable for biological/chemical material.
  Personal vehicle must be insured if transporting research samples.
  If shipping additional regulation apply and you must attend the “transport of hazardous material” provided by the Safety Office.
√
√
√
Transport of Research Material

## Slide 14
Non hazardous
Biological waste
Solid
Liquid
Sharp waste
Sharps and syringes
Hazardous chemical waste
As per COSHH risk assessment
Lab sink
Virkon
(tips and pipettes only)
Potentially
infectious waste (gloves)
GMO waste (autoclave bags)
Lab Waste Disposal
Duty of care
Legal requirement
Bring to waste room
Bring to glasswash

## Slide 15
New starter Microsoft Form
  Identify hazards
  HS1
  Access request
Intranet pages: https://www.ndcn.ox.ac.uk/about/professional-services/health-and-safety/health-and-safety-policies
iPassport, an account will be set up for you to access:
  Safety Policies
  HTA training record
  Biosafety training record
  Specialised training record
Documentation

## Slide 16
Any question?
Lab tour